## Slide 1
THESIS PROPOSAL | 10-MINUTE RECORDED PRESENTATION
Development of a Treatment Process for Potable Water Production Using Ceramic Membrane Filtration
A desk-based comparative evaluation
Central research question
How can ceramic membrane materials, fouling control and hybrid designs be combined into an evidence-based treatment train for potable water?
Secondary data • Systematic screening (Page et al., 2021) • Decision framework
[Student name] | [Student ID] | [Module / Supervisor]
2.2 billion
people lacked safely managed drinking water in 2022
WHO/UNICEF, 2023
73%
global coverage of safely managed drinking water in 2022 (31% in sub-Saharan Africa)
WHO/UNICEF, 2023
Long life
Ceramic membranes offer chemical and thermal stability, low fouling and long working life
Jarrar et al., 2024
Notes: Hello, and thank you for watching. My proposal is titled Development of a Treatment Process for Potable Water Production Using Ceramic Membrane Filtration. My central research question asks how ceramic membrane materials, fouling control and hybrid designs can be combined into an evidence-based treatment train for safe drinking water. I will answer it through a desk-based comparative evaluation of published data, which needs no laboratory work. The topic matters because safe water is a basic need, and treatment choices are complex. This presentation covers the background, rationale, methods, expected results, resources and timeline in turn.

## Slide 2
Background: safe drinking water is still limited, and ceramic membranes are a promising option
2.2 billion
people lacked safely managed drinking water in 2022, and global coverage was only 73% (WHO/UNICEF, 2023).
Membranes
increasingly complement coagulation, sedimentation and sand filtration (Jarrar et al., 2024); ceramics offer chemical and thermal stability and long life (Hosseinzadeh et al., 2025).
Full scale
Plants operate in Singapore, Japan, the United States, South Korea, the Netherlands, the United Kingdom and Switzerland, and look competitive long term (Akash et al., 2024).
Chart: Population using safely managed drinking water services, 2022 (%)
| Global | Europe and Northern America | Sub-Saharan Africa
Safely managed drinking water coverage, 2022 (%) | 73 | 94 | 31
Source: WHO/UNICEF (2023), Progress on household drinking water, sanitation and hygiene 2000–2022. Percentages as cited in the author's literature review.
Notes: Safe drinking water is still out of reach for many people. In 2022, 2.2 billion people lacked safely managed drinking water, and global coverage was 73 percent, but only 31 percent in sub-Saharan Africa, according to WHO and UNICEF, 2023. Membrane processes increasingly complement conventional treatment, and ceramic membranes stand out for chemical and thermal stability, low fouling and long working life, Jarrar and colleagues, 2024, and Hosseinzadeh and colleagues, 2025. Ceramic membranes are commonly made from alumina, zirconia, titanium dioxide or silicon carbide, each with different strength, chemical resistance and cost, Akash and colleagues, 2024. Full-scale plants already operate in countries including Singapore, Japan and the United Kingdom, and appear economically competitive over the long term, Akash and colleagues, 2024.

## Slide 3
Problem, gap and rationale: the evidence on ceramic membranes is scattered
Problem. Material choice, fouling control and contaminant removal are studied separately, so utilities lack a consistent basis for choosing a treatment train (Fu et al., 2024; Cai et al., 2023).
Known from research
Low-cost supports cut cost but may lose strength and pore uniformity (Fu et al., 2024)
Fouling raises energy use and lowers flux (Cai et al., 2023)
Ceramic log-reduction data are scarcer than for granular media (Burke et al., 2025)
Research gap
The literature review found no integrated comparison linking materials, fouling control, contaminant removal and sustainability to treatment-train selection. The Week 1–2 search will test this.
Who benefits. Utilities and engineers, researchers, regulators and communities lacking safe water. Supports Sustainable Development Goal 6 (United Nations, 2015).
Chart: Removal reported by single studies (%)
| Heavy metals (polymer-coated ceramic) | PFOA (Fe-based ceramic, one pass) | Microplastic alternatives, lower | Microplastic alternatives, upper
Reported removal (%) | 97 | 99 | 72 | 82
Sources: Azzam et al. (2025), heavy metals (reported as over 97%; plotted as 97); Chen et al. (2025), PFOA; Kim et al. (2025), alumina membranes. Different feeds, scales and conditions, so values are not directly comparable.
Notes: The problem is that the evidence is scattered. Material choice matters: low-cost waste-based supports cut costs but may reduce mechanical integrity and pore uniformity, Fu and colleagues, 2024. Fouling raises energy use and lowers flux, Cai and colleagues, 2023. Removal also depends on the contaminant. The chart shows single studies reporting over 97 percent heavy metal removal, about 99 percent PFOA removal, and 72 to 82 percent removal of microplastic alternatives. These studies used different conditions, so they cannot be ranked directly. A systematic review for WHO guidance found fewer ceramic log-reduction data than for granular media filtration, Burke and colleagues, 2025. My literature review found no integrated comparison linking these factors. Utilities, researchers and regulators would benefit, and the work supports Sustainable Development Goal 6, United Nations, 2015. Without a consistent comparison, a utility cannot easily choose between materials, hybrid designs and contaminant targets. That is why this project is needed now.

## Slide 4
Research aims, questions and conceptual framework
Aim: To build an evidence-based decision framework for ceramic membrane treatment trains that produce potable water.
Objectives
Compare materials and fabrication routes by strength, pore structure, cost and removal.
Evaluate fouling-control methods and hybrid configurations by flux, cleaning demand and removal.
Assess removal of metals, arsenic, PFAS, microplastics and pathogens; map weak evidence.
Develop a decision framework using performance, cost and sustainability criteria.
Research questions
RQ1: Which materials best balance strength, cost and removal?
RQ2: Which fouling-control and hybrid options perform best?
RQ3: How do sustainability and cost compare with polymeric and conventional options?
Conceptual framework
Materials and fabrication
Alumina, zirconia, waste-based (RQ1)
Fouling control and hybrids
Ozonation, conductive, ceramic–NF (RQ2)
Contaminant removal
Metals, arsenic, PFAS, microplastics, pathogens
Sustainability and cost
Chemicals, waste, CO₂, lifetime cost (RQ3)
Decision framework
Treatment train for potable water (SDG 6)
Author's framework, based on Cai et al. (2023), Hosseinzadeh et al. (2025) and Jarrar et al. (2024).
Notes: My aim is to build an evidence-based decision framework for ceramic membrane treatment trains. Four aims guide this: compare materials and fabrication routes; evaluate fouling control and hybrid configurations; assess removal of metals, arsenic, PFAS, microplastics and pathogens; and develop the framework itself. Three research questions ask which materials balance strength, cost and removal; which fouling-control and hybrid options perform best; and how sustainability and cost compare with polymeric and conventional options. The framework on the right links these steps. Each aim produces a concrete deliverable, so progress can be checked at each stage, and every research question links back to one or more aims.

## Slide 5
Methods: a desk-based comparative evaluation, and why it fits the question
1
Identify
Search Scopus, Web of Science and similar databases for studies from 2020 onwards.
Output: Candidate records
2
Screen
Apply inclusion and exclusion criteria, following PRISMA 2020 (Page et al., 2021).
Output: Screened set
3
Extract
Record material, pore size, feed water, pressure, scale, flux, rejection, fouling control and cost.
Output: Extraction matrix
4
Synthesise
Convert to common units; keep bench results apart from pilot and full-scale results.
Output: Comparison tables
5
Score
Rate configurations on removal, fouling control, strength, cost and sustainability; test weights.
Output: Ranked options
6
Frame
Match source water and priority contaminants to a recommended treatment train.
Output: Decision framework
Why appropriate. Many experiments exist; the gap is consistent comparison, which a desk-based synthesis delivers at zero cost.
Transparent and repeatable. Each step has a recorded output, so another researcher could repeat it (Page et al., 2021).
Source: Workflow designed by the author; screening and reporting adapted from Page et al. (2021).
Notes: My design is a desk-based comparative evaluation of published secondary data, in six steps. First, I identify studies from 2020 onwards in databases such as Scopus and Web of Science. Second, I screen them against clear criteria, following the PRISMA 2020 statement, Page and colleagues, 2021. Third, I extract performance data into a standard matrix. Fourth, I convert units and compare by scale. Fifth, I score configurations and test the weights. Sixth, I build the decision framework. This suits the question because many experiments already exist, and the gap is consistent comparison, which I can achieve at zero cost. I chose this design for three reasons. It is realistic within six weeks, it carries no safety or ethical risk, and it makes my reasoning transparent and repeatable. A laboratory study would test only a few membranes, whereas a synthesis can compare many materials and contaminants together.

## Slide 6
Data sources, selection criteria, quality control and ethics
Source group | Examples from the literature review
Materials and fabrication | Fu et al. (2024); Bahrouni et al. (2025); El Azizi et al. (2025)
Fouling and hybrids | Cai et al. (2023); Xie et al. (2024, 2025); Lin et al. (2024)
Contaminants | Azzam et al. (2025); Chen et al. (2025); Kim et al. (2025); Burke et al. (2025)
Sustainability and cost | Hosseinzadeh et al. (2025); Akash et al. (2024)
Access context | WHO/UNICEF (2023)
Quality control. Re-extract 10% of records after one week and compare. Grade conclusions by evidence strength and scale, because test conditions differ and positive results are published more often. Keep an audit log of every screening decision.
Include
Published 2020 onwards
Ceramic membranes for water treatment
Quantitative data on flux, rejection, fouling, strength, energy, cost or life cycle
Peer-reviewed or WHO/UNICEF
Exclude
Opinion pieces
Non-English papers
Duplicate records
No usable performance data
Ethics. Only published sources are used. No people or animals are involved, so ethical risk is low. Ethics status will be confirmed with the supervisor in Week 1.
Sources: author's literature review (cited works as listed); Page et al. (2021) for screening. Selection criteria designed by the author.
Notes: Sources are peer-reviewed articles on materials, fouling, contaminants and sustainability, plus the WHO and UNICEF report. I include studies of ceramic membranes for water treatment that report quantitative data such as flux, rejection, strength, energy or cost. I exclude opinion pieces, non-English papers and duplicates. For quality control, I will re-extract ten percent of records after one week and compare them. Because test conditions differ and positive results are published more often, I will grade conclusions by evidence strength and scale. The extraction matrix records material, pore size, feed water, operating pressure, test scale, flux, rejection, fouling control and cost indicators. The scoring matrix then rates each configuration on removal, fouling control, strength, cost and sustainability, and I vary the weights to see whether rankings stay stable. Ethically, I use only published sources, with no people or animals, and I will confirm ethics status with my supervisor in week one.

## Slide 7
Expected results, outcomes and benefits
Known from previous research
Ceramic–nanofiltration hybrids removed more organic carbon and divalent ions than nanofiltration alone (Xie et al., 2025).
Ozonation can reduce cleaning frequency (Xie et al., 2024).
Conductive membranes are promising but unproven at scale (Lin et al., 2024).
Expected from this study (anticipated, not yet established)
Hybrids will outperform standalone membranes for organic carbon and divalent ions.
Waste-based membranes will be cheaper but more variable (Fu et al., 2024).
Largest evidence gaps: PFAS, microplastics and viruses at full scale (Burke et al., 2025).
Key outcomes and benefits
Outputs
Extraction database, comparison tables, evidence-gap map and decision framework.
Utilities and engineers
A clear guide for selecting ceramic membrane treatment trains.
Researchers and regulators
A prioritised map of gaps for emerging contaminants (Burke et al., 2025).
Communities
Better technology choices may support affordable supply (WHO/UNICEF, 2023).
Sources: Burke et al. (2025); Fu et al. (2024); Lin et al. (2024); WHO/UNICEF (2023); Xie et al. (2024, 2025). Anticipated findings are expectations, not results.
Notes: Now, expected results. I want to separate what is known from what I expect. Known: hybrid ceramic and nanofiltration systems removed more organic carbon and divalent ions than nanofiltration alone, Xie and colleagues, 2025; ozonation can reduce cleaning frequency, Xie and colleagues, 2024; and conductive membranes are promising but unproven at scale, Lin and colleagues, 2024. Anticipated, but not yet established: I expect hybrids to outperform standalone membranes, waste-based membranes to be cheaper but more variable, and the largest evidence gaps to be PFAS, microplastics and viruses at full scale. The outputs are a database, comparison tables, a gap map and a decision framework, benefiting utilities, researchers, regulators and underserved communities. Any evidence that contradicts these expectations will be reported openly. Better treatment choices may also support affordable supply for communities lacking safe water, WHO and UNICEF, 2023.

## Slide 8
Budget, resources and personnel: no funds requested
Resource | Detail | Cost ($)
Student researcher | About 150 hours of coursework time | 0
Supervisor | About 12 hours within normal supervision | 0
Librarian | About 3 hours of university service | 0
Database access | Existing university subscriptions | 0
Software | Free reference manager; existing spreadsheet | 0
Computer and storage | Existing equipment | 0
Laboratory consumables | None required for a desk-based design | 0
Total | Overall project cost | 0
Costs are low because published data remove the need for equipment, consumables, participants and travel. Time is the main input and is shown in hours, not dollars.
Personnel and responsibilities
Student researcher: designs the protocol; searches, screens and extracts data; builds the framework; writes the report.
Supervisor: reviews the protocol, scoring matrix and draft; confirms ethics status.
Librarian (optional): advises on database access and search strategy.
Source: Resource plan designed by the author for a desk-based study using published data (Page et al., 2021). Hours are estimates.
Notes: No funds are requested, so the overall budget is zero dollars. The study uses published data and existing university resources: library database access, a free reference manager, a spreadsheet and my own computer. No laboratory consumables are needed. My time, about 150 hours, is the main input. For personnel, I conduct the research, my supervisor reviews the protocol, scoring matrix and draft and confirms ethics status, and a librarian may advise on search strategy. Costs are low because secondary data removes the need for equipment, consumables, participants and travel. Every item uses an existing resource, which is why the budget is zero. I will confirm database access with the university library.

## Slide 9
Six-week timeline and milestones
Task
Wk 1
Wk 2
Wk 3
Wk 4
Wk 5
Wk 6
Protocol, search strategy, ethics check
Database search and screening
Data extraction and quality check
Normalisation and comparison tables
Scoring matrix and sensitivity test
Decision framework and gap map
Report writing, referencing, submission
Milestones
Wk 1: ethics status confirmed
Wk 2: final record set agreed
Wk 4: scoring matrix complete
Wk 6: report submitted
Why it is realistic
Scope is limited to published studies from 2020 onwards, which one researcher can screen and extract in this period, and each stage has a checkable output.
Source: Timeline designed by the author around the screening and synthesis steps of Page et al. (2021). Amber bar = final reporting stage.
Notes: The timeline is six weeks. Week one covers the protocol, search strategy and ethics check, and searching begins. Weeks two and three cover screening and data extraction. Weeks three to five cover comparison, scoring, the sensitivity test and the framework. Weeks five and six cover report writing, referencing and submission. Milestones are the final record set in week two, the scoring matrix in week four, and submission in week six. The scope is realistic because it covers only published studies from 2020 onwards, which one researcher can screen and extract within six weeks, and each stage produces a checkable output.

## Slide 10
Conclusion and key takeaway
What I will investigate
How ceramic membrane materials, fouling control and hybrid designs combine into a treatment train for potable water.
Why it matters
2.2 billion people lack safely managed drinking water (WHO/UNICEF, 2023), and ceramic membrane evidence is scattered (Fu et al., 2024).
How I will do it
A transparent desk-based synthesis of published data, screened and reported following PRISMA 2020 (Page et al., 2021).
Expected contribution
A practical, evidence-based decision framework and gap map for utilities, researchers and regulators, supporting SDG 6 (United Nations, 2015).
Key takeaway: a consistent, transparent comparison turns scattered ceramic membrane evidence into practical choices for safe drinking water.
Notes: To conclude, I propose to compare published evidence on ceramic membrane materials, fouling control, hybrid designs and contaminant removal, and turn it into a decision framework for potable water treatment. It matters because 2.2 billion people still lack safely managed drinking water, WHO and UNICEF, 2023. The method is transparent, low risk and costs nothing. I expect it to give utilities and researchers a clear, evidence-based guide. In short: what I will investigate is how best to combine ceramic membrane options; why it matters is safe water and scattered evidence; how I will do it is a transparent desk-based synthesis; and the contribution is a practical decision framework. Thank you for listening.

## Slide 11
Reference list (APA 7th edition)
Akash, F. A., Shovon, S. M., Rahman, W., Rahman, M. A., Chakraborty, P., Prasetya, T. A. E., & Monir, M. U. (2024). Advancements in ceramic membrane technology for water and wastewater treatment: A comprehensive exploration of current utilizations and prospective horizons. Desalination and Water Treatment, 319, Article 100569. https://doi.org/10.1016/j.dwt.2024.100569
Azzam, N. M., Ali, S. S., Mohamed, G. G., Omar, M. M., & Amin, S. K. (2025). Fabrication of composite ceramic polymeric membranes for agricultural wastewater treatment. Scientific Reports, 15, Article 2330. https://doi.org/10.1038/s41598-025-85542-w
Bahrouni, J., Attia, A., Elberrichi, F. Z., Dammak, L., Baklouti, L., Ben Aissa, M.-A., Ben Amar, R., & Deratani, A. (2025). Green and sustainable clay ceramic membrane preparation and application to textile wastewater treatment for color removal. Membranes, 15(10), Article 292. https://doi.org/10.3390/membranes15100292
Burke, M., Wells, E., Larison, C., Rao, G., Bentley, M. J., Linden, Y. S., Smeets, P., DeFrance, J., Brown, J., & Linden, K. G. (2025). Systematic review of microorganism removal performance by physiochemical water treatment technologies. Environmental Science & Technology, 59(41), 21763–21775. https://doi.org/10.1021/acs.est.4c03459
Cai, C., Sun, W., He, S., Lu, P., Zhang, J., & Liang, H. (2023). Ceramic membrane fouling mechanisms and control for water treatment. Frontiers of Environmental Science & Engineering, 17(10), Article 126. https://doi.org/10.1007/s11783-023-1726-9
Chen, S., Qiu, L., Yu, X., Shen, X., Wang, X., Wang, J., Zhang, Y., Chu, L., Zhang, M., Zhou, Z., Wang, Y., Ma, H., Gu, C., & Chen, Z. (2025). Renewable Fe-based ceramic membrane for efficient per- and polyfluoroalkyl substances (PFAS) removal with light-driven regenerative ability. Separation and Purification Technology, 379, Article 134948. https://doi.org/10.1016/j.seppur.2025.134948
El Azizi, A., El Harouachi, H., Ahoudi, D., Maliki, S., Mansori, M., & Loutou, M. (2025). Phosphate tailings and clay-based ceramic membranes: Tailoring microstructure and filtration properties via alkali activation. Membranes, 15(2), Article 52. https://doi.org/10.3390/membranes15020052
Fu, Z., Zhou, Z., Liu, Z., Yang, H., & Chen, Z. (2024). Feasibility and challenges of low-cost ceramic membranes in water treatment applications. Desalination and Water Treatment, 320, Article 100739. https://doi.org/10.1016/j.dwt.2024.100739
Hosseinzadeh, F., Hashemi, H., & Sarpoolaky, H. (2025). Sustainable ceramic membrane for water and wastewater treatment: A comprehensive review of environmental, social, and economic aspects. Desalination, 615, Article 119231. https://doi.org/10.1016/j.desal.2025.119231
Jarrar, R., Abbas, M. K. G., & Al-Ejji, M. (2024). Environmental remediation and the efficacy of ceramic membranes in wastewater treatment—A review. Emergent Materials, 7, 1295–1327. https://doi.org/10.1007/s42247-024-00687-0
Kim, S. Y., Kim, S., & Park, C. (2025). Evaluation of ceramic membrane filtration for alternatives to microplastics in cosmetic formulations using FlowCam analysis. Membranes, 15(1), Article 35. https://doi.org/10.3390/membranes15010035
Lin, Z., Liu, L., Zhang, C., Su, P., Zhang, X., Li, X., & Jiao, Y. (2024). Emerging conductive ceramic membranes for water purification and membrane fouling mitigation. Chemical Engineering Journal, 493, Article 152568. https://doi.org/10.1016/j.cej.2024.152568
Page, M. J., McKenzie, J. E., Bossuyt, P. M., Boutron, I., Hoffmann, T. C., Mulrow, C. D., Shamseer, L., Tetzlaff, J. M., Akl, E. A., Brennan, S. E., Chou, R., Glanville, J., Grimshaw, J. M., Hróbjartsson, A., Lalu, M. M., Li, T., Loder, E. W., Mayo-Wilson, E., McDonald, S., … Moher, D. (2021). The PRISMA 2020 statement: An updated guideline for reporting systematic reviews. BMJ, 372, Article n71. https://doi.org/10.1136/bmj.n71
United Nations. (2015). Transforming our world: The 2030 Agenda for Sustainable Development (A/RES/70/1). https://sdgs.un.org/2030agenda
WHO/UNICEF. (2023). Progress on household drinking water, sanitation and hygiene 2000–2022: Special focus on gender. World Health Organization and United Nations Children's Fund.
Xie, X., Wang, L., Wei, J., He, H., Guo, Z., Wang, C., Wen, X., & Song, Y. (2024). Progress in ceramic membrane coupling ozonation process for water and wastewater treatment: A critical review. Chemical Engineering Journal, 493, Article 152475. https://doi.org/10.1016/j.cej.2024.152475
Xie, Y., Liu, Z., Yu, J., Shan, Z., Liu, H., & Zhang, Y. (2025). Water purification efficiency and membrane fouling behavior of ceramic membrane–nanofiltration in treating water treatment plant production wastewater. Membranes, 15(12), Article 387. https://doi.org/10.3390/membranes15120387
Notes: The references cited on the slides are listed here in APA seventh edition. The full list is in the written proposal.